| CSEE TYPE UM71 TRACK CIRCUIT HISTORY CARD |
| --- |
| LENGTH: m | m | FREQUENCY: | Hz | TRACK: |  |
|  | TRANSMITTER END | RECEIVER END |  |  |  |
| Date | Tx Serial No | Tx Input to MU (E1/E2) (V) | TU or MU V1/V2 (V) | DC Volts A+ / A- (V) | Rx Serial No | Rx TU V1/V2 (V) | Rx Input (9/10 on MU) (V) | VR1/R2 |  |  | KR v | PSU Serial No | DC Volts A+/ A- (V) | Drop Shunt (Ω) | 0.15Ω Shunt Test | Ballast Condition | Signature of Testing Officer |
|  |  |  |  |  |  |  |  | Unoccupied (mV) | With shunt on (mV) | Zero Feed (mV) |  |  |  |  |  |  |  |

*Measure with Selective Meter or with Adjacent Tx Disconnected

Rx Connections Type T1	Tx Connections Type T1

| FREQ Hz | KEM | CONNECT | BRIDGE |
| --- | --- | --- | --- |
|  |  | 1 on Mu to | 2 on Mu to |  |
| 1700 | 3,5 | V2 | V7 | V3 - V4 V5 - V6 |
| 2300 | 4 | V7 | V8 |  |
| 2000 | 3,75 | V1 | V7 | V3 - V4 V5 - V6 |
| 2600 | 4,25 | V1 | V8 | V2 - V7 |

| KRV | CONNECT | BRIDGE |  | KRV | CONNECT | BRIDGE |  | KRV | CONNECT | BRIDGE |  | KRV | CONNECT | BRIDGE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | R1 to | R2 to |  |  |  | R1 to | R2 to |  |  |  | R1 to | R2 to |  |  |  | R1 to | R2 to |  |
| 1 | R3 | R4 |  |  | 20 | R9 | R4 | R3 - R8 |  | 39 | R10 | R5 | R3 - R9 |  | 58 | R10 | R7 | R4 - R6 R5 - R8 |
| 2 | R5 | R4 |  |  | 21 | R9 | R8 |  |  | 40 | R10 | R5 | R4 - R9 |  | 59 | R10 | R7 | R3 - R6 R5 - R8 |
| 3 | R3 | R5 |  |  | 22 | R9 | R3 | R4 - R8 |  | 41 | R10 | R4 | R3 - R9 |  | 60 | R10 | R5 | R3 - R8 |
| 4 | R5 | R7 | R3 - R6 |  | 23 | R9 | R4 | R5 - R8 |  | 42 | R10 | R9 |  |  | 61 | R10 | R5 | R4 - R8 |
| 5 | R5 | R7 | R4 - R6 |  | 24 | R9 | R3 | R5 - R8 |  | 43 | R10 | R3 | R4 - R9 |  | 62 | R10 | R4 | R3 - R8 |
| 6 | R4 | R7 | R3 - R6 |  | 25 | R9 | R5 | R3 - R6 R7 - R8 |  | 44 | R10 | R4 | R5 - R9 |  | 63 | R10 | R8 |  |
| 7 | R6 | R7 |  |  | 26 | R9 | R5 | R4 - R6 R7 - R8 |  | 45 | R10 | R3 | R5 - R9 |  | 64 | R10 | R3 | R4 - R8 |
| 8 | R3 | R7 | R4 - R6 |  | 27 | R9 | R4 | R3 - R6 R7 - R8 |  | 46 | R10 | R5 | R3 - R6 R7 - R9 |  | 65 | R10 | R4 | R5 - R8 |
| 9 | R4 | R7 | R5 - R6 |  | 28 | R9 | R6 | R7 - R8 |  | 47 | R10 | R5 | R4 - R6 R7 - R9 |  | 66 | R10 | R3 | R5 - R8 |
| 10 | R3 | R7 | R5 - R6 |  | 29 | R9 | R3 | R4 - R6 R7 - R8 |  | 48 | R10 | R4 | R3 - R6 R7 - R9 |  | 67 | R10 | R5 | R3 - R6 R7 - R8 |
| 11 | R9 | R7 | R3 - R8 R5 - R6 |  | 30 | R9 | R4 | R5 - R6 R7 - R8 |  | 49 | R10 | R6 | R7 - R9 |  | 68 | R10 | R5 | R4 - R6 R7 - R8 |
| 12 | R9 | R7 | R4 - R8 R5 - R6 |  | 31 | R9 | R3 | R5 - R6 R7 - R8 |  | 50 | R10 | R3 | R4 - R6 R7 - R9 |  | 69 | R10 | R4 | R3 - R6 R7 - R8 |
| 13 | R9 | R7 | R3 - R8 R4 - R6 |  | 32 | R10 | R7 | R5 - R6 R3 - R9 |  | 51 | R10 | R4 | R5 - R6 R7 - R9 |  | 70 | R10 | R6 | R7 - R8 |
| 14 | R9 | R7 | R6 - R8 |  | 33 | R10 | R7 | R5 - R6 R4 - R9 |  | 52 | R10 | R3 | R5 - R6 R7 - R9 |  | 71 | R10 | R3 | R4 - R6 R7 - R8 |
| 15 | R9 | R3 | R4 - R7 R6 - R8 |  | 34 | R10 | R7 | R4 - R6 R3 - R9 |  | 53 | R10 | R7 | R5 - R6 R3 - R8 |  | 72 | R10 | R4 | R5 - R6 R7 - R8 |
| 16 | R9 | R4 | R5 - R7 R6 - R8 |  | 35 | R10 | R7 | R6 - R9 |  | 54 | R10 | R7 | R5 - R6 R4 - R8 |  | 73 | R10 | R3 | R5 - R6 R7 - R8 |
| 17 | R9 | R3 | R5 - R7 R6 - R8 |  | 36 | R10 | R7 | R3 - R6 R4 - R9 |  | 55 | R10 | R7 | R4 - R6 R3 - R8 |  |  |  |  |  |
| 18 | R9 | R5 | R3 - R8 |  | 37 | R10 | R7 | R4 - R6 R5 - R9 |  | 56 | R10 | R7 | R6 - R8 |  |  |  |  |  |
| 19 | R9 | R5 | R4 - R8 |  | 38 | R10 | R7 | R3 - R6 R5 - R9 |  | 57 | R10 | R7 | R3 - R6 R4 - R8 |  |  |  |  |  |