| WB&S FS2500 TRACK CIRCUIT HISTORY CARD |
| --- |
| TRACK |  |  | IMPEDANCE BONDS |
| LENGTH | metres |  | RESONATED | Y/N |
| FREQUENCY | Hz |  | RES.CAP. | nF |
| Tx OUTPUT LEVEL | % HI/LO |  | CAP. VOLTS | V |

| DATE | TRANSMITTER END | DPU* | RECEIVER END | 0.15Ω Shunt Check (OK) | Ballast Condition | Signature of Testing Officer |
| --- | --- | --- | --- | --- | --- | --- |
|  | Tx Serial No | TU Input (V) | TU T1/T2 (V) | PSU Serial No | DC (V) | DPU Serial No | Amp Serial No | Amp Gain (Hi/Lo) | Rx Input Current (mA) | Rx Serial No | TU T1/T2 (V) | Rx Input (V) | Monitor Volts | Rx Sens | Drop Shunt (Ω) | PSU Serial No | DC (V) |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | Unoc- cupied (mV) | With shunt on (mV) | Zero Feed (mV) |  |  |  |  |  |  |  |

*For tracks with Intermediate Receivers Only

RECEIVER SENSITIVITY ADJUSTMENT TABLE	GUIDE TO Tx OUTPUT LEVEL ADJUSTMENT

| SENS | CONNECT | BRIDGE |  | Nominal Track Circuit Length | Tx Output Level | Output Number | Terminals Used* |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | A to | B to |  |  |  |  |  |  |
| 1.65 | -45 | +5 | +45 to -15 | +15 to -5 |  | 50 - 250 m | 20% | 1 (LO) | 1 and 2 |
| 1.60 | -45 | +15 | +45 to -15 |  |  | 250 - 450 m | 40% | 2 | 1 and 3 |
| 1.55 | -45 | -5 | +45 to -15 | +15 to +5 |  | 450 - 600 m | 60% | 3 | 3 and 4 |
| 1.50 | -45 | +5 | +45 to -5 |  |  | 600 - 750 m | 80% | 4 | 2 and 4 |
| 1.45 | -45 | +45 |  |  |  | 750 - 900 m | 100% | 5 (HI) | 1 and 4 |
| 1.40 | -45 | -5 | +45 to +5 |  |  | * The screen terminal is earthed |
| 1.35 | -45 | +5 | +45 to +15 | -15 to -5 |  |  |  |
| 1.30 | -45 | -15 | +45 to +15 |  |  |  |  |  |  |
| 1.25 | -45 | -5 | +45 to +15 | -15 to +5 |  |  |  |  |  |
| 1.20 | -15 | +5 | +15 to -5 |  |  |  |  |  |  |
| 1.15 | -15 | +15 |  |  |  |  |  |  |  |
| 1.10 | -15 | -5 | +15 to +5 |  |  |  |  |  |  |
| 1.05 | -5 | +5 |  |  |  |  |  |  |  |
| 1.00 | B |  |  |  |  |  |  |  |  |
| 0.95 | +5 | -5 |  |  |  |  |  |  |  |
| 0.90 | +15 | +5 | -15 to -5 |  |  |  |  |  |  |
| 0.85 | +15 | -15 |  |  |  |  |  |  |  |
| 0.80 | +15 | -5 | -15 to +5 |  |  |  |  |  |  |
| 0.75 | +45 | +5 | -45 to -15 | +15 to -5 |  |  |  |  |  |
| 0.70 | +45 | +15 | -45 to -15 |  |  |  |  |  |  |
| 0.65 | +45 | -5 | -45 to -15 | +15 to +5 |  |  |  |  |  |
| 0.60 | +45 | +5 | -45 to -5 |  |  |  |  |  |  |
| 0.55 | +45 | -45 |  |  |  |  |  |  |  |
| 0.50 | +45 | -5 | -45 to +5 |  |  |  |  |  |  |
| 0.45 | +45 | +5 | -45 to +15 | -15 to -5 |  |  |  |  |  |
| 0.40 | +45 | -15 | -45 to +15 |  |  |  |  |  |  |
| 0.35 | +45 | -5 | -45 to +15 | -15 to +5 |  |  |  |  |  |