RAIL BREAK REPORT

For reporting broken rails, welds and insulated joints

Part 1, to be completed on track (Note: If a particular box or field is not applicable, leave blank)

| REPORTING BROKEN: | RAIL |  | WELD |  | INSULATED JOINT |  | Date of break: |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| LINE: |  | Location: |  | km | Base code: |  |
| --- | --- | --- | --- | --- | --- | --- |

| GPS Settings (if known): | Latitude |  | Longitude |  | Proximity to fixed points: |  |
| --- | --- | --- | --- | --- | --- | --- |
| Track: | Single |  |  |
|  | Double |  |  | Up |  | Down |  |  |
|  | Loop |  |  | Other (describe) |  |

| Rail: | Left/Dn |  | Right/Up |  | For Known Defect, show number: |  |
| --- | --- | --- | --- | --- | --- | --- |
| In curve: | High |  | Low |  | In dual gauge: | Common |  | Standard |  | Broad |  |

| Plain line: |  | In P&C: |  | If in P&C describe component & location: |  | Cast crossing |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| Rail Section: | Less than 40 kg |  | 40/41kg |  | 47kg |  | 50kg |  | 53kg |  | 60kg |  | Other (describe) |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Rail Type: | Standard carbon |  | Head hardened |  |
| --- | --- | --- | --- | --- |

| Rail Head Height either side of break: |  | mm (left) |  | mm (right) |
| --- | --- | --- | --- | --- |
| Rail Width: |  | mm |  |  |
| Fastening type: | Dogspikes |  | Resilient |  |

| Sleeper type: | Timber |  | Concrete |  | Steel |  | Mixed |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Sleeper condition each side of break: | Good for 5 yrs or more |  | Poor (Broken/rotten) |  |
| --- | --- | --- | --- | --- |

| Sleeper support condition each side of break: | Good |  | Pumping over 1 or 2 sleepers |  |
| --- | --- | --- | --- | --- |
|  | Pumping over 3 or more sleepers |  |
| Ballast degradation: | Mud hole |  | Powdered ballast |  | OK |  |
| Rail surface: | Spalling |  | Shelling |  | Rolling contact fatigue |  | Wheel burns |  | OK |  |
| Vertical geometry of nearest welds both sides of break (1m straight edge): | Weld 1 |  | mm | Dip |  | Peak |  |
|  | Weld 2 |  | mm | Dip |  | Peak |  |
| Estimated air temperature at time of break: |  | °C | Gap at break: |  | mm |

If broken rail: Advise manufacturer, month & year rolled, heat number and ingot letter (usually on other side of rail standard and month & year rolled) and should be a letter from A to F etc.

| Manufacturer: |  | Heat Numbers: |  | Ingot Letter: |  |
| --- | --- | --- | --- | --- | --- |

| If broken weld, type: | Thermic |  | Flash Butt |  | Manual Arc |  | Junction Weld |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Welder’s identification mark, name, or weld number: |  |
| --- | --- |

If the rail or weld was previously marked, details of weld and defect numbers:

Show position of break and defect (if any) on diagrams

If break is at or within 100mm from a weld, show weld on diagram and distance of break from weld.

If broken insulated joint: Describe break (eg pull apart, broken fishplates) and if available manufacturer and insulated joint number.

| Method of finding break: | Visual by Infrastructure staff |  | Signal Failure |  | Train Crew |  |
| --- | --- | --- | --- | --- | --- | --- |
| Other (describe) |  |

| Break found by: |  | Time found: |  | Date: |  |
| --- | --- | --- | --- | --- | --- |

| TCR Number: |  |
| --- | --- |

| Describe the defect and the cause if known: |  |
| --- | --- |

| Attach photos of break taken in field |
| --- |
| <<insert photo - press F1 for help>> | <<insert photo - press F1 for help>> | <<insert photo - press F1 for help>> |
| Photo 1 | Photo 2 | Photo 3 |
| Inspector: |  | (print name) |

| Signed: |  | Date: |  |
| --- | --- | --- | --- |

Part 2, to be completed in the office

| Date of last continuous ultrasonic rail inspection: |  |
| --- | --- |

| Was rail surface shielding reported on last continuous ultrasonic rail inspection? | Yes |  | No |  |
| --- | --- | --- | --- | --- |
| Was a defect at break reported on last continuous ultrasonic rail inspection? | Yes |  | No |  |

| Stress free temperature at break location (if known): |  | °C | Verse measurement: |  | °C |
| --- | --- | --- | --- | --- | --- |

| Ellipse Defect Number: |  |
| --- | --- |

If cause or break is immediately apparent, no further investigation required.

For breaks of an unusual or complex nature, or the cause is not apparent from visual inspection or a pattern of breaks on a particular line section is becoming apparent, further investigation is required.

Results of investigation, including metallurgical tests if required.

| <<insert link to report - press F1 for help>> | <<insert link to report - press F1 for help>> |
| --- | --- |
| Report 1 | Report 2 |
| Note: to open the hyperlink the document must be unprotected – go to Tools > Unprotect Document |

| Investigation Report Break Cause: |  |
| --- | --- |

| Area Manager Comments: |  |
| --- | --- |

Area Manager Sign and Date:

| Additional Photos: |
| --- |
| <<insert photo - press F1 for help>> | <<insert photo - press F1 for help>> | <<insert photo - press F1 for help>> |
| Photo 4 | Photo 5 | Photo 6 |

Note: Attach or insert more detailed photographs of break if it is considered that the defect may have been detectable during the last continuous ultrasonic rail inspection, or for forwarding details of complex or unusual broken rails to continuous ultrasonic inspection Contractor.

| Break details entered onto database and form filed by: |  | (Name) |
| --- | --- | --- |

|  | (Position) | Date: |  |
| --- | --- | --- | --- |