| Welder's Name |  |  | Supervisor's Name |  |
| --- | --- | --- | --- | --- |
| Welder ID number | Company Name: |  | Supervisor's Signature | Date: / / |
| Welder's Signature | Date: / / |  | Project or RCRM |  |

| WELD LOCATION | WELD DETAILS | Track Condition | PRESERVING EXISTING SFT | Weld Collar Vertical Misalignment <4mm | FINISHED WELD GEOMETRY |
| --- | --- | --- | --- | --- | --- |
| Date | Track/SPN or equipment number | Km (each weld) | Rail Leg U/D | Rail Size | Rail Mismatch | Weld Type | Method of Rail Cut | Machine No.(FB) Or Batch No (AT) | Weld number (where applicable) |  | Rail out = Rail in < 2mm |  | Peak 0.0 to 0.5mm | Lateral 0.0 to 0.5mm | Ramp angle < 7 mr |
|  |  |  |  |  |  |  |  |  |  |  | Punch Marks | Rail Temp 0C |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  | Before | After |  |  |  |  |  |

Notes/comments:

Tick check box to confirm the following has been undertaken:

- Each weld has been visually inspected.

- Excess mould sand has been cleaned.

- Each weld properly packed and adequately supported.

Track Condition

Good condition

Track pumping

Poor top

Poor alignment

Bog hole

High rail wear

Other

Examples of track condition descriptor.